## Slide 1: Troubleshooting guide
Guangzhou Shirui Electronics Co., Ltd
--X3 S series

## Slide 2
Agenda
Schematic Diagram
Turn-on failure
Display issue
PC issue
Touch issue
Camera&MIC issue

## Slide 3
Schematic Diagram-S series

## Slide 4
Schematic Diagram-U series

## Slide 5
2. Turn-on failure

## Slide 6
Turn-on procedure
CN2
CN16
CN16
CN2

## Slide 7
Failure 1 – No red light
Description:
The power supply is normal, but the power light is not bright and the screen can not be started.
Analysis procedure:
1. Check key appearance. Is there damage ?
2. Open the back cover, check related Pin voltage.
3. Replace Main power board, TV main board, key board, AC connector board
Notes: If there is a interrupt when upgrade MCU, it will also cause this failure. You should upgrade MCU via VGA interface.

## Slide 8
Failure 2 – Can not turn blue
Description:
Press the power key in standby mode. Key can not turn green.
Analysis procedure:
1. Try both power button and Remote Controller.
2. Confirm there is no device connected the USB of TV Main Board.
3. Open the back cover. Main power board, TV main board, key board
4. Replace the related cable.

## Slide 9
3. Display issue

## Slide 10
Failure 1 – No backlight
Description:
No backlight after we start up screen
Analysis procedure:
1. Check power LED status. If it breathe in red and blue slowly, it is in power saving mode.
2. TV main board BL_ON is abnormal. Re-upgrade TV firmware or replace the TV main board.
3. Power board defect. Replace the Main power board.
4. Backlight defect. Replace the panel.

## Slide 11
Failure 2 – No display
Description:
Backlight is ON, but screen is black without any display.
Analysis procedure:
1. Re-upgrade firmware, TV main and MCU.
2. Check, TCON power supply status. If there is abnormal, solve it.
3. Replace the TV main board, TCON board. You can use HDMI-OUT to help confirm.
4. Replace the video signal cables.
5. Opencell issue, replace the panel

## Slide 12
Failure 3 – Abnormal Display (Flicker / Blurry)
Description:
Backlight is ON, but screen is flickering or blurry.
Analysis procedure:
1. Re-upgrade firmware, TV main and MCU.
2. Re-connect the video signal cables.
3. Replace TCON board.
4. You can also use HDMI-OUT to help to confirm.
5. Opencell issue, replace the panel

## Slide 13
4. PC issue
1) Upgrade PC firmware and TV main firmware
2) Check the PC module status, replace the PC module
3) Replace the TV board

## Slide 14
5. Touch issue

## Slide 15
Touch signal flow-S series
U Series: P-CAP panel and EMR panel are connected with USB HUB board, the HUB board is connected with TV board.
Notes: 原理图加安坐模块

## Slide 16
Failure 1 – No touch at all
Description:
Touch can not work at all
Analysis procedure:
1. Reboot the machine or init TV/ Replace touch pens(U series).
2. Re – upgrade TV firmware and touch firmware.
3. Re - connect the touch cable.
4. Replace the touch board, TV main board/ Replace P-CAP control board or EMR control board , USB hub board(U Series) .
5. Replace the panel(U series)
Notes: 原理图加安坐模块

## Slide 17
Failure 2 – Touch abnormal
Description:
1. touch can not work in some area.
2. line is not continuous.
3. writing is recognized as eraser.
Analysis procedure:
1. Re-upgrade touch firmware and TV main firmware.
2. Replace touch frames/ Replace P-CAP control board or EMR control board.
Notes: 原理图加安坐模块

## Slide 18
Camera issue:
1. Firmware related issue, Upgrade TV main firmware or camera firmware
2. Replace the TV main board, Camera board, Camera
3. Replace USB HUB FFC cable
MIC issue:
1. Firmware related issue, Upgrade TV main firmware or MIC firmware
2. Replace the TV main board, Camera board, MIC board
3. Replace USB HUB FFC cable or MIC FFC cable.
7. Camera&MIC Issue
Notes: 原理图加安坐模块

## Slide 19
Thank you