## Slide 1: MAXHUB Wireless Screen share Introduction & FAQ
Customer Service Center
5/27/2019

## Slide 2: Catalog
Hardware Introdution
Software Functions
Troubleshooting
FAQ
Notes: 硬件介绍：
传屏器SM01，传屏盒子
软件功能：
传屏器传屏，交替传屏，四分屏，启用触摸，启用扩展屏，mac开启权限，

## Slide 3: Hardware Introduction

## Slide 4
Mirroring Dongle-SM01/WT01
One button mirroring design
Touch reverse control & Extend screen
Transmit video, audio & touch signals
Support 4 split windows in one screen*，each window can be controlled individually
5G frquency，stable and credible
Low consumption, No extra Power Supply, 15m transmitting distance
Support Windows7、 MacOS 10.10 and above.
8 Maximum connecting PC clients at the same time and can switch to any one smoothly
Notes: 待新品发布后，需要补充WT01和WT02的硬件参数信息

## Slide 5
Mirroring Dongle-SM01/WT01
Show/Hide the mouse cursor
Eable/Disable the touch signal
Eable/Disable extended screen
ON/OFF Keep the aspect ratio
SM04 can be directly used with a MAXHUB unit.
Steps:
1.pair SM04 with a MAXHUB unit.
2. Plug the SM04 into the USB port of your laptop. Install the driver and then you can use it.
With the UWST control software of SM04 in your laptop, you can do following settings:

## Slide 6
Mirroring Box-WB01
Support 4K@60fps HDMI output
Double HDMI output ports
Support 2.4G/5G wirelss hotspot
Support POE power supply
Support Touch signal transmission
Support timing control
Support centralized control & remote management
Support OTA
Notes: 待补充，接口示意图，接口输出的介绍

## Slide 7
Supported Client Device
Mobile device：
support 5G WIFI
support 802.11 a/c WLAN
Mobile system：
Andriod phones：Android 5.0 and above
IPhone：IOS9.0 and above
PC Hardware：
support 5G WiFi
PC System：
Windows：Windows 7 and above
Mac：OS10.10 and above
Notes: 待补充，接口示意图，接口输出的介绍

## Slide 8
Configuration of WB01
Preparation:
PC with wireless network card or Mobile phones connecting with WB01
Enter the manage console:
Input the manage address of WB01 in the browser of your PC or mobile phone:
http://10.10.10.50:8090
It will ask you to set password the first time logging in. Just skip this step.
Notes: 待补充，接口示意图，接口输出的介绍

## Slide 9
Ethernet network：
Check the MAC address
Choose the IP acquire mode: automatic or manual
Settings of WB01
Notes: 待补充，接口示意图，接口输出的介绍

## Slide 10
Wireless hotspot：
Switch for 5G and 2.4G
Show/Hide SSID of the hotspot
Other basic wireless network settings
Notes:
You can open 5G and 2.4G hotspots at the same time but you can just close one at a time.
Settings of WB01
Notes: 待补充，接口示意图，接口输出的介绍

## Slide 11
Display settings:
1. Keep the HDMI output activated all the time or just when mirroring the image of your device.
2. Configure the resolution of the HDMI output. Default resolution is 1080p@60Hz
3.Custom background of desktop.
Settings of WB01
1
2
3
Notes: 待补充，接口示意图，接口输出的介绍

## Slide 12
Timing setting：
Configure auto start up and shut down plan.
Settings of WB01

## Slide 13
Tools: USB disk (FAT32 format)
Method:
1. Download the upgrade file and copy it to the root directory of USB disk. Do NOT unzip the file.
2.Start up the WB01. Plug in the USB disk. It will upgrade automatically.
Factory reset
1. Do factory reset in the setting menu.
2. Pull out the power cable of WB01 and press the power button and hold. Plug in the power cable and keep on holding the power button for at least 10 seconds.
Firmware Upgrade Method for WB01
Notes: 待补充，接口示意图，接口输出的介绍

## Slide 14: Software Functions

## Slide 15
Sofware Introduction
Slipe right at Homepage, you will see the screen share software fast start introduction. You can download and install the corresponding client you need.
Notes: 待补充，接口示意图，接口输出的介绍

## Slide 16
software screen share
Working Principle
encoding
Software Screen share
Application
Receiver-WB01
Receiver & Display-MAXHUB
Display Devices
Hardware Screen share
private protocol
Airplay
HDMI
private wireless
protocol
encoding

## Slide 17
The screen share dongle(SM01) connects with PC through USB port.( Shown as USB Mass Storage, Human Interface Devices)
The internal network card of the dongle conects with the MAXHUB's hotspot through WiFi(802.11 a/g/n) protocol.
When you open the USWT software on your desktop, the programm will capture the images of screen and encode them.
After encoding the screenshots, the programm pass the information to SM01 through USB HID interface.
The dongle(SM01) transmits the encoded data to MAXHUB or the Screen Share Box-WB01
The MAXHUB or WB01 will decode the data and output the audio , video and touch signals.
Working Process
Notes: 待补充，接口示意图，接口输出的介绍

## Slide 18
Comparasion Between different Screen Share functions
Notes：the functions may change along with the upgrade of firmware
 | Andriod Phone +Screen share | Apple IOS+ Screen share | MAC+Airplay | MAC+SM01 | Windows+Screen Share | Windows+SM01
Audio signal | N | Y | Y | Y | Y | Y
Conection Method | Hotspot of MAXHUB | Hotspot of MAXHUB | Hotspot of MAXHUB | Hotspot of MAXHUB | Hotspot of MAXHUB or the same LAN with MAXHUB | Hotspot of MAXHUB
Touch signal | N | N | N | Y | Y | Y
Extended Screen | N | N | Y | N | Y | Y
Four splitted-Screen | Y | Y | Y | Y | Y | Y

## Slide 19
Notes:
Andriod Screen Share can not transfer the audio signal but IOS client can.It is the code limitation of andriod root system.
Make sure the android system can get on-line, so that the mobilephones, Pads or computers connecting with the hotspot of MAXHUB can get on-line as well.
Support 8 maximum clients connected with one MAXHUB panel at the same time.And 4 split screen at most.And you need to long hold the button on the dongle to join the screen share if there have been other connections.
The screen share software for PC can only be used on MAXHUB X3 series.Connecting with the hotspot of MAXHUB or in the same LAN with MAXHUB, both ways can make your PC share screen.
Notes: 待补充，接口示意图，接口输出的介绍

## Slide 20: Troubleshooting

## Slide 21
Troubleshooting Steps
Problems: SM01 can not connect with MAXHUB/WB01 BOX, stop working during screen sharing or can not detect the MAXHUB/WB01 BOX
Steps:
1. Do not cover the WiFi antennas of MAXHUB or WB01 box with any material.
2. Check if there are any interference signals or the WiFi restraint (WIDS/WIPS) setted by IT engineer of customer's company.
3. Change another PC to test if there is something wrong with the PC being used.
3. upgrade the firmware of TV board ,PC module and WB01 box to the latest version. Rematch the dongle with MAXHUB or WB01.
4. Check the hotspot settings. Use your mobilephone to connect with the hotspot, check if it works well. If it works, replace the SM01. If not, replace the TV board.
Notes: 待补充，接口示意图，接口输出的介绍

## Slide 22
Software Information
1.If you can not solve the problem in the end, please get the information below and send to the technical support team.
SN of the MAXHUB unit, firmware version, video of problem.
2.For the problem of Screen share software, we need more information like the software version, the models of PC or mobilephone being used
3. For the problem with SM01 dongle, please send the log files. You can find the files in below address
windows: C:/Users/user/AppData/Roaming/MaxhubDongleClient/
Mac: ~/Library/Logs/MaxhubDongleClient/
Notes: 待补充，接口示意图，接口输出的介绍

## Slide 23: FAQ

## Slide 24
1.Description: The signal transmitted between SM01 and MAXHUB/WB01 is interrupted frequently.( every 10 mins)
Solutions：Check if the router has turned on the WIDS/WIPS function. You can ask the IT manager of customer's company.
Reason：The WIDS/WIPS function will cut down the signal frequently.
2.Description：The anti-virus software may recognize the driver of SM01 as virus, and stop the driver from runing.
Solutions：Clarify to customer that it is a false alarm. And recommand to add the driver into the white list of their anti-virus software.
Screen Share FAQ
Notes: 待补充，接口示意图，接口输出的介绍

## Slide 25
3.Description：Fail to screen share, and error code is (0)
Solutions：
1.It means the SM01 can not connect with the hotspot of MAXHUB/ WB01. Please test the hotspot with your mobilephone.
2.Check if the WIDS/WIPS function interfere the signal.
3.Replace SM01 and the TV board at last.
Screen Share FAQ
Notes: 待补充，接口示意图，接口输出的介绍

## Slide 26
4.Description：Fail to screen share, and error code is (-7)
Solutions：
It means that the SM01 could connect with the hotspot, but the receiver software of MAXHUB/WB01 does not work.
1. Check the Taskmanager of the MAXHUB windows system. If you can not see the “ MaxhubAirReceiver.exe” process, please try to reinstall the firmware for PC .
2. Close the firewall of windows system of MAXHUB. Pay attention to the third party firewall software installed by customers.
3.Pull out the PC module and rematch the SM01. If it works, the problem may caused by the network setting between the android and windows system.
Screen Share FAQ
Notes: 待补充，接口示意图，接口输出的介绍

## Slide 27
6. Description: Failed to pair the SM01 with MAXHUB or WB01. It shows “fail”message or nothing on the screen.
Solutions：
1.If shows nothing, please do factory reset and reinstall the firmware for TV board and PC module.
2.If shows “fail” message, check if the hotspot is turned on. And confirm that the hotspot can work well with your computer or mobilephone.
5.Description: When insert the SM01 into the USB port of MAXHUB to upgrade,the upgrade process stops half way.
Solutions：
1.Need to upgrade the SM01 manually.
Screen Share FAQ
Notes: 待补充，接口示意图，接口输出的介绍

## Slide 28
7.Description: When connect WB01 with a external screen, the screen display “no signal”
Solutions：
1.Modify the output resolution of WB01 to a lower one.
2.Check the HDMI cable and replace another one.
3. Use a PC to test the external screen. If works, please replace the WB01.
Screen Share FAQ
Notes: 待补充，接口示意图，接口输出的介绍

## Slide 29
8.Description: The signal of WB01 breaks down several times during screen sharing.
Solution
1. upgrade the firmware to the latest one.
2. Avoid covering the antenna with metal. And please do not put high-power electronic equipment around the WB01. Do not put thick obstacle between WB01 and your computer.
3.Change another laptop to check, if works, please check the difference between the two PCs.
4. Check with your mobilephone to see it will break down. If not, please replace the WB01 and SM01 one by one.
Screen Share FAQ
Notes: 待补充，接口示意图，接口输出的介绍

## Slide 30: Thanks
www.maxhub.vip