## Slide 1: MAXHUB Network FAQ
Albert Yang

## Slide 2: Content
Network Structure
Network Configuration
Troubleshooting Guide
FAQ
Notes: 硬件介绍：
传屏器SM01，传屏盒子
软件功能：
传屏器传屏，交替传屏，四分屏，启用触摸，启用扩展屏，mac开启权限，

## Slide 3: Network Structure

## Slide 4
MAXHUB X3 Network Structure
TV Board+PC module:
PC module will use the LAN port and SI02 dongle to get online(Just like our laptop to use LAN cable and WiFi)
PC module will share its network to Android system through interal USB network card.Now the Android system only connect with internal local network whose DNS is 192.168.153.1, and it doesn't connect with the external network directly.
SWITCH
Ethernet
Wireless
Notes: 待新品发布后，需要补充WT01和WT02的硬件参数信息

## Slide 5
Only Android without PC module:
The LAN port and SI02 dongle will switch to android system. And the Android system will connect to the external network directly.
MAXHUB X3 Network Structure
SWITCH
Ethernet
Wireless
Notes: 待新品发布后，需要补充WT01和WT02的硬件参数信息

## Slide 6: Network Configuration

## Slide 7
X3 Wireless - Auto obtain IP/Fixed IP
Notes: 待补充，接口示意图，接口输出的介绍

## Slide 8
X3 Ethernet - Auto obtain IP/Fixed IP
Notes: 待补充，接口示意图，接口输出的介绍

## Slide 9: Troubleshooting Guide

## Slide 10
X3 Network status checking
Cable network status
Wireless network status
1.Related with the network of android system.
2.Should be auto obtain IP address
Notes: 待补充，接口示意图，接口输出的介绍

## Slide 11: FAQ

## Slide 12
Description：PC module can get online, but TV board or wireless hotspot can't.
solution：
please reinstall the PC suite program.
If still not work,please replace the TV board.
Notes: 待补充，接口示意图，接口输出的介绍

## Slide 13
Descrion：When using windows pc+ screen share software, the PC can't share screen after inputing the codes.
Solution：
Ping the IP address of MAXHUB and check if the network connection is worked between the laptop and MAXHUB. If the firewall software is opened in the laptop, please turn it off.
If you can't ping to the MAXHUB,please check with local IT engineer to check the network connection. If you can ping to the MAXHUB,but fail to share screen, then the LAN port used by Screen share software maybe disabled. Please ask IT engineer to open below ports:
Type | Range
TCP&UDP | 7382-7435
Notes: 待补充，接口示意图，接口输出的介绍

## Slide 14
Description：MAXHUB+PC module, connect with wireless network, the network speed is very slow.
Solution：
1.Check the WiFi signal intensity. The signal will be ok if its intensity is in the range of -50~-70dbm. Recommand to use WirelessMon software.
2.If the signal is not strong enough, please check the wireless router or AP with IT engineer.
3.Please make sure the firmware version is above 3.4.0. Lower version may have network bug.
Notes: 待补充，接口示意图，接口输出的介绍

## Slide 15
Description：Sider bar not working property.Not respond when click the setting button or homepage button.
Solution：
1.Check the status of USB network card and make sure it obtain the IP and DNS automatically.
2.Check if the main version and minor version are match with each other. Upgrade to the latest version.
Notes: 待补充，接口示意图，接口输出的介绍

## Slide 16
Description：Customer ask to add MAXHUB to network white list to get online.
Solution：
Check the MAC address from below location, and add both of them to the white list of router.
Notes: 待补充，接口示意图，接口输出的介绍

## Slide 17: Thanks
T 020 8207 5661
www.maxhub.vip